## Slide 1
1
Inverter Voltage
Simulation
60191844
최준환

## Slide 2
01
Introduction
1.1 기존 시뮬레이션 방식
  Single Half Bridge Inverter
  Controlled Current Source
  No load

## Slide 3
01
Introduction
1.2 새로운 시뮬레이션 방식
  Another Inverter for Current Source
  Higher DC Voltage
  RL Load

## Slide 4
02
Circuit Details
2.1 Components and Parameters
  Minimum Resistance (10 μΩ) for Every Resistor
  Including IGBT, Diode
  Parasitic Capacitance: 4 nF
  Load Inductance: 0.2 H
  DC Voltage: 300V (Load INV) , 500V (Generating INV)
  Switching Frequency: 10K
  Dead time: 2 μs

## Slide 5
03
Current Control
3.1 Equivalent Circuit Analysis
  Load INV 를 역방향 전압원으로 보고 분석
  Load INV 항을 포함한 RL회로의 전류제어
  PI Controller 활용
  Feed-Forward (전향보상향)을 통한 Load INV 항 제거
  Average Voltage output during 1 Switching period
  INV를 고정 전압원으로 본다
  -> 주파수 조절이 필요 할 수 있음

## Slide 6
03
PI Controller Details
3.2 Parameters
  Anti-Windup: -250~250 V (-Vdc/2 ~ Vdc/2)
  Duty output

## Slide 7
04
Result
4.1 Current
  Response time: about 0.05s
  Current Ripple: about 0.037 A
0.037A
0.05s

## Slide 8
04
Result
4.2 Voltage
  Duty는 0.04초 까지 0출력
  -> 0.5초 부터 0.01 단위로 0.01초 마다 증가
  -> 0.96초부터 1출력
  Dead time 침범을 고려한 출력 설정
  Duty가 0.02 바뀔때마다 1 step 씩 증가
  3~4V의 오차가 고정적으로 발생
Duty.csv

## Slide 9
04
Result
4.3 Problems
  Plecs의 solver와 소자들의 고유값을 변경
  -> 전류 튀는 현상 해결
  그래프가 반대방향인 이유
  전류 방향 설정이 반대
  기존 그래프: 인버터에서 나가는 방향이 +
  새로운 그래프: 인버터로 들어오는 방향이 +
  New Problem
  듀티 출력전압 반응성 (0.02단위 변화) why?
  오차가 전류의 극성에 따라 비대칭 why?